## Slide 1: SMART INDIA HACKATHON 2026
Problem Statement ID - SIH26175
Problem Statement Title - Single-View Height Estimation and 3D Flythrough
Theme - Disaster Management
PS Category – Software
Team ID - [Registered Team ID]
Team Name (Registered on portal) - TerraVista_iitrpr
Idea Title - DepthWizard

## Slide 2: IDEA TITLE
DepthWizard: From One Satellite Image to Measurable 3D Terrain Intelligence
INPUT
Single RGB satellite image
AI
Height-above-ground estimation
CALIBRATE
DEM / terrain context
OUTPUT
3D terrain + height products
ACTION
Flood / slope / affected structures
HOW IT ADDRESSES THE PROBLEM
• Single optical image is the primary input.
• Generates height and terrain products without a new stereo/LiDAR survey for every use case.
• PNG/JPG → relative DSM; GeoTIFF → metric geospatial DSM after calibration.
• Standard GeoTIFF outputs support rapid analysis and offline/standalone use.
WHY DEPTHWIZARD IS DIFFERENT
• Satellite-native AI rather than a ground-image-only depth approach.
• Height-above-ground (nDSM / AGL) estimation with terrain calibration.
• GSD-aware inference with uncertainty outputs, not just visual depth.
• Integrated flood, slope/landslide, viewshed and affected-building tools.
INNOVATION & UNIQUENESS
Satellite-native AI
nDSM / AGL height
GSD + uncertainty
Disaster analytics
TerraVista

## Slide 3: TECHNICAL APPROACH
Pipeline: From Pixels to Terrain Intelligence
INPUT
RGB satellite image
PREPROCESS
Metadata / GSD / tiling
AI MODEL
DINOv3 satellite encoder + height decoder
CHMv2 / DPT height decoder
HEIGHT
nDSM / AGL height +
uncertainty map
CALIBRATE
DEM fusion + terrain context
OUT DSM + 3D
AI / ML
• PyTorch + Hugging Face
• DINOv3 satellite-pretrained backbone
• CHMv2 / DPT height decoder
• GSD conditioning + TTA / Gaussian tile blending
• ONNX Runtime for CPU inference
GEOSPATIAL
• GDAL, Rasterio, PyProj
• GeoTIFF / float32 DSM processing
• DEM fusion + datum correction
• CartoDEM / SRTM / Copernicus
APPLICATION & OUTPUTS
• GeoTIFF DSM + relative height outputs
• glTF / GLB 3D model + terrain tiles
• React + Three.js / WebGL viewer
• Flood / slope / viewshed analysis
• FastAPI / REST / CLI + Tauri desktop
Modular AI + geospatial processing + interactive visualization • Validation: RMSE / MAE + ICESat-2
TerraVista
Chart: Projected height error vs GSD (RMSE, m)
| 0.3 m | 0.5 m | 1.0 m | 2.0 m | 5.0 m
With GSD conditioning | 1.8 | 2 | 2.4 | 3.1 | 4.3
Without conditioning | 1.9 | 2.6 | 3.8 | 5.4 | 7.6
Chart: Est. inference time / 1024x1024 tile (s)
| GPU (CUDA) | CPU (ONNX) | CPU (PyTorch)
Seconds | 0.4 | 2.1 | 6.8
Chart: Est. training cost (GPU-hours)
| Full fine-tune | Partial unfreeze | Frozen backbone
GPU-hours | 120 | 45 | 18

## Slide 4: FEASIBILITY AND VIABILITY
Grounded in Open Data, Modular Software and Practical Deployment
FEASIBILITY
• Established open-source AI/geospatial stack.
• DFC2019 / US3D and GAMUS provide development and validation starting points.
• Frozen backbone keeps training cost and memory requirements low; fine-tune on a modern/cloud GPU.
• Tiling + optimized inference support large satellite imagery.
VIABILITY
• Modular pipeline permits model upgrades without rewriting the app.
• Standard GeoTIFF output fits existing GIS workflows.
• ONNX Runtime + Tauri enable CPU-based standalone offline deployment.
• Compatible fallback monocular-depth model reduces model-weight availability risk.
CHALLENGE → RISK → MITIGATION
CHALLENGE
RISK
MITIGATION
Varying GSD
Inconsistent estimates
GSD conditioning + multi-resolution training
Monocular ambiguity
Uncertain absolute height
nDSM / AGL prediction + terrain calibration
Sparse reference data
Limited validation
Multiple datasets + ICESat-2 validation
Large imagery
Memory limits
Overlapping tiles + efficient blending
Limited GPU / internet
Deployment limits
ONNX CPU inference + offline demo data
TerraVista
Chart: Est. share of height uncertainty
| GSD variation | Monocular ambiguity | DEM / datum offset | Tile blending seams | Sensor & atmospheric
Share | 0.3 | 0.25 | 0.2 | 0.15 | 0.1

## Slide 5: IMPACT AND BENEFITS
Terrain Intelligence That Supports Real-World Decisions
DEPTHWIZARD
Terrain + height intelligence
DISASTER MANAGEMENT
Flood mapping • slope/landslide • affected-building counts
URBAN PLANNING
Building heights • 3D terrain where elevation is missing
REMOTE SENSING
More value from existing optical archives • less reliance on repeated stereo/LiDAR surveys
RECONNAISSANCE
Terrain visualization • viewshed analysis
ECONOMIC
Lower dependence on costly multi-sensor surveys
SOCIAL
Faster, more accessible emergency terrain intelligence
ENVIRONMENTAL
Supports terrain, canopy and flood/landslide analysis
ONE SATELLITE IMAGE → TERRAIN INTELLIGENCE → FASTER DECISION SUPPORT
TerraVista
FROM TERRAIN DATA TO ACTIONABLE INTELLIGENCE
1
HEIGHT MAP
nDSM / AGL
2
3D TERRAIN
DSM / GeoTIFF
3
DECISION
Flood / Slope
One optical observation → measurable terrain context

## Slide 6: RESEARCH AND REFERENCES
Research Foundation: Models, Datasets and Validation
MODELS & METHODS
• DINOv3 Satellite Pretraining - Hugging Face / Meta AI
• CHMv2 Canopy Height Model - model + research paper
• Depth Anything 3 - arXiv:2511.10647
• Depth2Elevation - IEEE TGRS, 2025
• HTC-DC Net - remote-sensing height-estimation research
DATASETS / VALIDATION / OFFICIAL SOURCES
• DFC2019 / US3D and GAMUS datasets
• SRTM 30m / Copernicus DEM GLO-30
• CartoDEM - ISRO Bhuvan
• ICESat-2 ATL08 / ATL03 for reference and validation
• ISRO Bhoonidhi / Bhuvan and ISPRS Vaihingen / Potsdam
Research basis: monocular height estimation • DSM generation • geospatial calibration • ICESat-2 validation • terrain rendering | Evaluation: RMSE / MAE
TerraVista
EVIDENCE → DATA → TERRAIN REFERENCE → QUANTITATIVE VALIDATION
MODELS
DINOv3 + CHMv2
DATASETS
DFC2019 + GAMUS
TERRAIN REFERENCE
CartoDEM / SRTM / Copernicus
VALIDATION
RMSE / MAE + ICESat-2
Chart: Validation targets: height accuracy by terrain class (ICESat-2 / DEM reference)
| Flat urban | Dense urban | Vegetated | Hilly / mixed
RMSE (m) | 1.9 | 3.2 | 4.1 | 3.6
MAE (m) | 1.2 | 2.1 | 2.8 | 2.4