## Slide 1: SMART INDIA HACKATHON 2026
Problem Statement ID - SIH26175
Problem Statement Title - Single-View Height Estimation and 3D Flythrough
Theme - Disaster Management
PS Category – Software
Team ID - [Registered Team ID]
Team Name (Registered on portal) - TerraVista_iitrpr
Idea Title - DepthWizard
Notes: We are TerraVista from IIT Ropar. Our idea, DepthWizard, answers SIH26175: single-view height estimation and 3D flythrough for disaster management.

## Slide 2: IDEA TITLE
DepthWizard: One Satellite Image → 3D Heights You Can Fly Through and Check
INPUT
PNG / JPG / TIFF / GeoTIFF
AI HEIGHT
Height above ground, every pixel
CALIBRATE
Cleaned 30 m DEM + ICESat-2 → metres
VERIFY
Held-out laser check + click-to-measure
FLY & ACT
3D flythrough + flood / slope tools
HOW IT MEETS THE PROBLEM STATEMENT
✓ One optical image in: no stereo pair, LiDAR or InSAR needed
✓ PNG/JPG → relative DSM · GeoTIFF → absolute DSM in metres
✓ Upload → auto-process → fly through the reconstructed 3D terrain
✓ Click any building: height with a 90% interval (too narrow above 10 m)
✓ Working prototype: runs offline on an 8 GB laptop; GeoTIFF + GLB export
WHY DEPTHWIZARD IS DIFFERENT
• Published RS3DAda model: zero-shot on GAMUS, paper reproduced on ATL / ARG
• Numbers with a baseline or 95% CI: GAMUS MAE 3.90 m vs 5.65 m flat ground
• Laser check that is not circular: ICESat-2 passes split into levelling / checking
• Trust layer: 90% building interval (misses tall blocks) + consistency score
• Disaster scenarios on top: flood depth, routes, relief sites, slope classes
INNOVATION & UNIQUENESS
Remote-sensing height AI
Real metres, laser-levelled
Checked vs LiDAR + 2 lasers
Bird's-eye → street flythrough
TerraVista
Notes: One satellite image goes in and heights come out, and this works in our prototype today. The height model is RS3DAda, published at NeurIPS 2024; we run the released weights and have not fine-tuned it. For a GeoTIFF, the terrain comes from the free 30 m Copernicus model with buildings and trees removed using our heights, and it is levelled with NASA ICESat-2 laser points when at least two laser passes cross the scene. The user flies through the town and clicks a building to see its height with a 90% interval; we say on screen that the interval is too narrow for buildings over 10 m. Every accuracy number we show is listed in docs/CLAIMS.md with a baseline or published reference, and with a 95% confidence interval where it averages several tiles or scenes. GAMUS is our only zero-shot test; the Overhead Geopose cities were in the model's unlabelled adaptation data, so there we only check that we reproduce the paper.

## Slide 3: TECHNICAL APPROACH
Pipeline: Pixels → Height → Metres → Checked 3D
INPUT
RGB image (PNG / JPG / TIFF)
PREPROCESS
Read GSD + CRS · overlapping 518 px tiles
AI MODEL
RS3DAda (DINOv2 ViT-L + DPT), released weights
HEIGHT
Height above ground + consistency score
CALIBRATE
VERIFY
GLO-30 terrain, buildings removed, laser-levelled
Held-out laser check + error report
OUT DSM + 3D
AI / ML
✓ RS3DAda (NeurIPS 2024): released weights, no tuning
✓ 4-flip TTA · blended 518 px tiles · 8 GB laptop
✓ 90% building interval (split-conformal, GAMUS)
✓ Zero-shot: GAMUS · paper reproduced: ATL / ARG
• Planned: DINOv3 / CHMv2 challenger, ONNX CPU model
GEOSPATIAL
✓ Rasterio · PyProj; GeoTIFF in / out; EGM2008
✓ DSM = terrain (GLO-30; CartoDEM drop-in) + height
✓ ICESat-2 levelling needs 2+ passes; GEDI checks
✓ Validate: raster, survey points, held-out laser
• Planned: Cartosat + CartoDEM (data requested)
APPLICATION & 3D VIEWER
✓ Three.js viewer; GLB + GeoTIFF export
✓ Free-fly (WASD), draw-a-path auto-fly, video export
✓ Street-level camera · • Sat3DGen mesh (planned)
✓ Click-to-measure; flood, route, relief-site tools
✓ Offline laptop app (.bat) · • Tauri app (planned)
✓ working in our prototype today • planned, not built | every number: docs/CLAIMS.md, with its baseline or 95% CI
TerraVista
Chart: SCENARIO TEST: Porto Alegre 2024 flood (CSI)
| Raw 30 m DEM (GLO-30) | + our building removal | + ICESat-2 laser levelling | FABDEM (reference)
CSI | 0.2 | 0.3 | 0.79 | 0.32
Scenario test, not a forecast: pre-flood image, 4 windows (320 m) vs IPH-UFRGS extent; levelled before the 2-pass rule.
PROTOTYPE: flood fly-through, saved as MP4
Our viewer: drone path over Canoas (Brazil) at the May 2024 flood level; orange = roofs still above water
Chart: GAMUS MAE per tile (m): ours blue, flat ground grey
| Buildings | Trees | Road | Ground
Ours | 3.55 | 6.67 | 1.82 | 0.86
Flat ground (0 m) | 9.08 | 8.7 | 1.72 | 0.46
150 GAMUS tiles (aerial 0.33 m, zero-shot): MAE 3.90 m [3.24, 4.66] vs 5.65 flat ground. Leafless trees; tall objects too low.
Notes: Ticks mark what works in our prototype; bullets are planned and not built. The model is RS3DAda with its released weights: we did not fine-tune it, and the DINOv3 / CHMv2 challenger, the ONNX model and the Tauri app are plans. Left chart: a scenario test on the May 2024 Porto Alegre flood. From the pre-flood image we flooded the terrain to the gauge level in 4 small windows that have laser data and compared with the IPH-UFRGS flood extent: raw 30 m DEM CSI 0.20, with our building removal 0.30, after ICESat-2 levelling 0.79; FABDEM scores 0.32. It is a spot check, not a forecast, and it was run before we stopped levelling from a single laser pass, which would now skip one of the four windows. Right chart: GAMUS, the dataset the PS recommends; it is aerial imagery at 0.33 m, not satellite. On 150 tiles our mean MAE is 3.90 m [3.24, 4.66], against 5.65 m for predicting flat ground everywhere. On open ground predicting zero is still better; trees, mostly leafless in these photos, and tall buildings read too low (bias -7.6 m for 10 to 20 m objects).

## Slide 4: FEASIBILITY AND VIABILITY
Built on a Released Model, Free Data and Offline-Ready Software
FEASIBILITY
• Working today: released RS3DAda end to end, 42 s for a test scene on an 8 GB laptop
• Test data in hand: GAMUS, Overhead Geopose ATL / ARG, 8 Indian laser scenes
• Free terrain + truth data: Copernicus GLO-30, ICESat-2, GEDI, OpenStreetMap
• Not yet: Cartosat + CartoDEM (login-gated; request drafted to PS owner / NRSC)
VIABILITY
• Modular: swap the height model without touching calibration or the viewer
• Standard outputs: GeoTIFF DSM with the input CRS, GLB 3D mesh, building JSON
• Offline today on a laptop (.bat launcher); ONNX model + Tauri app planned
• Licences: code MIT / Apache; weights trained on CC BY-NC data; FABDEM checks only
CHALLENGE → RISK → MITIGATION
CHALLENGE
RISK
MITIGATION
New image resolution (GSD)
Wrong height scale
Read GSD from metadata · resampling tested (no gain): kept native
One image can't see ground level
Heights off in metres
Remove buildings from terrain · ICESat-2 levelling only from 2+ passes
Few tall buildings in training data
Tall buildings under-estimated
Report bias by height (-7.6 m at 10–20 m) · recalibration tried, not shipped
Tilted (off-nadir) images
Leaning buildings, shifted roofs
Planned: off-nadir test set + warning in UI (not built)
No GPU / no internet in the field
Tool unusable
Offline laptop app with CPU fallback (built) · ONNX model planned
TerraVista
Chart: MEASURED: published RS3DAda reproduced (MAE, m)
| ATL: source-only | ATL: paper | ATL: ours | ARG: source-only | ARG: paper | ARG: ours
MAE | 7.26 | 5.67 | 5.99 | 2.65 | 2.01 | 1.94
Geopose satellite tiles, 300 per city; adaptation domain, not zero-shot. 95% CI: ATL [5.57, 6.43], ARG [1.86, 2.03] m. Source-only, paper: published.
Notes: Everything we depend on is public: the model weights, GAMUS, Overhead Geopose, the Copernicus elevation model, ICESat-2 and GEDI. The chart checks that we run the model correctly: on 300 satellite test tiles per city from the Overhead Geopose challenge (cities whose unlabelled images the model adapted to, so this is a reproduction, not a zero-shot test) our MAE is 5.99 m in Atlanta and 1.94 m in Buenos Aires, against 5.67 and 2.01 published; both published values are inside our 95% intervals. The risks we measured: tall buildings read too low on every test set, and an isotonic correction made one held-out city worse, so we did not ship it. Resampling the input to another resolution gave no gain. We have not yet run on Cartosat or compared with CartoDEM; both need a login, and we have drafted a data request.

## Slide 5: IMPACT AND BENEFITS
From One Image to Faster, Verifiable Disaster Decisions
DEPTHWIZARD
Checked 3D from one image
DISASTER MANAGEMENT
Flood-depth scenarios · slope classes · affected buildings · routes, relief sites
Scenario test, Porto Alegre 2024: CSI 0.79 in 4 laser-levelled windows
URBAN PLANNING
Building heights (GAMUS: MAE 3.57 m on 1,450 buildings) · 3D base maps
REMOTE SENSING (ISRO)
More value from optical archives · next: test on Cartosat + CartoDEM
FIELD RESPONSE
Fly-through + street-level view for briefings · offline routes and relief sites
ECONOMIC
Reuse existing images instead of new LiDAR/stereo surveys for every event
SOCIAL
Faster 3D damage picture; works offline in the field
ENVIRONMENTAL
Terrain and slope context for flood and landslide planning
ONE SATELLITE IMAGE → CHECKED 3D → FASTER DECISIONS
TerraVista
FROM TERRAIN DATA TO ACTIONABLE INTELLIGENCE
1
HEIGHT MAP
per pixel
2
CHECKED 3D
metres + ICESat-2
3
DECISION
flood / slope
One optical image → measured, checked terrain context
Notes: In our Porto Alegre scenario test, starting from pre-flood images, the flood map matched the IPH-UFRGS flood extent with CSI 0.79 in the 4 small windows that had laser data; it is a scenario check, not a forecast, and the levelling predates our two-pass rule. Planners get building heights where no LiDAR exists: on GAMUS, building heights are off by 3.57 m on average, against 10.54 m for assuming flat ground. ISRO would get more value from existing optical images; the next step is to run on Cartosat, which we have requested.

## Slide 6: RESEARCH AND REFERENCES
Research Foundation: Published Model, Open Data, Independent Laser Checks
MODELS & METHODS
• RS3DAda: Song et al., NeurIPS 2024 (the model we run, released weights)
• Split-conformal: Angelopoulos & Bates 2021 (90% building interval)
• FABDEM: Hawker et al. 2022 (bare-earth DEM, used for checks)
• Roof photons in ICESat-2: Cai et al. 2024 (OSM footprints mask roofs)
• Reviewed, not built: DINOv3 / CHMv2, Prompt2DEM, Sat3DGen
DATASETS / VALIDATION / OFFICIAL SOURCES
• GAMUS (PS-recommended; aerial 0.33 m) · Overhead Geopose ATL / ARG
• Copernicus GLO-30 · FABDEM · CartoDEM (requested from NRSC)
• NASA ICESat-2 ATL03 / ATL08 · GEDI L2A · OpenStreetMap buildings
• IPH-UFRGS 2024 flood map · DFC2019 (adaptation domain, not zero-shot)
• Metrics: MAE, RMSE, bias, NMAD, r on nDSM; 95% CI over tiles / scenes
Not yet validated: Cartosat / CartoDEM, leaf-on canopy, intervals for tall buildings, floor counts, GCP accuracy, processing time
TerraVista
MODELS
RS3DAda (DINOv2)
DATASETS
GAMUS + Geopose
TERRAIN REFERENCE
GLO-30 / FABDEM
VALIDATION
ICESat-2 + GEDI
Chart: MEASURED: Indian scenes vs NASA lasers (8; GEDI 7), MAE (m): ours blue, baseline grey
| Height vs ICESat-2 | Height vs GEDI | DSM vs GEDI tops | DSM vs ICESat-2
Ours | 4.85 | 9.93 | 5.97 | 9.14
Baseline | 8.25 | 16.89 | 8.39 | 8.06
Baseline: height 0 (left two) or raw Copernicus DSM (right two). Ours loses on the last one.
Chart: MEASURED: 90% interval coverage, held-out city (%): DC blue, NYC teal, PHL orange
| LiDAR 3–10 m | LiDAR 10–20 m | LiDAR > 20 m
DC | 99.63 | 67.33 | 13.64
NYC | 99.33 | 49.12 | 30
PHL | 100 | 95.7 | 25
GAMUS LiDAR, leave-one-city-out, 959 blocks. Target 90%: met for low blocks, missed for tall ones.
Notes: Every method here is published and cited, and both charts are our own measurements. Left: eight Indian scenes against NASA lasers, with laser passes split so that nothing is checked on the photons used for levelling. Our heights above ground are off by 4.85 m against ICESat-2 (8 scenes) where assuming no height gives 8.25 m, and 9.93 against 16.89 m with GEDI (7 scenes). Our absolute DSM beats the raw Copernicus DSM against GEDI canopy and roof tops (5.97 vs 8.39 m) but not against all ICESat-2 photons (9.14 vs 8.06 m). Right: the 90% interval we show on each building, tested on a city it was not calibrated on. It covers low buildings almost always, but only 49 to 67% of 10 to 20 m blocks in New York and Washington and fewer above 20 m, which is why the viewer warns about tall buildings. Not yet validated: Cartosat and CartoDEM, leaf-on canopy, floor counts, ground-control-point accuracy and processing time.